## Slide 1: Single Precision Floating Point ALU in Verilog
Divyank Beniwal • Sagnik Majumdar Pereira Smith • Aaryan Garg

## Slide 2: Introduction
Let’s introduce you to our project.
1

## Slide 3: IEEE-754 Format:
The IEEE-754 Single Precision Floating point format is used to represent a large range of numbers with limited computational or storage resources.
The numbers are stored in 32 bits, where the first bit denotes the sign, the next 8 denote the exponent, and the rest of them denote the mantissa.

## Slide 4: ALU
An Arithmetic-Logic Unit (ALU) is a combinational digital electronic circuit and represents the fundamental building block of the Central Processing Unit (CPU) of a computer.
An ALU performs Addition, Subtraction, Multiplication, Division and Bitwise logical operations such as AND, OR, NOT on numbers in the IEEE-754 format.

## Slide 5: Conversion of Decimal to Floating Point
Placing Signed Bit
Place a signed bit (0 for +ve, 1 for -ve)
Then exponent value followed by mantissa.
Decimal to Binary
Convert Decimal to Binary form.
Shift radix point until there remains only one bit to the left.
Mantissa and Exponent
Number after the radix is mantissa.
If radix is shifted X times then exponent value is 127+X (in binary)

## Slide 6: Addition/Subtraction operations:

## Slide 7: Multiplication operations:

## Slide 8: Major Challenges Faced
Challenges during learning Verilog due to limited Internet facilities and frequent power-cuts.
Novice errors in writing the Verilog code due to a lot of Compile-time errors and writing the wrong code.
Underflow and Overflow troubled our multiplier and divider module quite a lot throughout testing. It was significantly reduced though.

## Slide 9: Architecture
Let’s discuss the architecture of our modules.
2

## Slide 10: Adder-Subtractor Module:
We have implemented the FP32 rules of addition and subtraction in this module.
We then checked the result for Underflow and Overflow.
This module had an accuracy of 99.75% on the test bench.

## Slide 11
This is the Block diagram of the complete Adder-Subtractor Module

## Slide 12: Addition-Normalizer Module:
We normalized the resulting mantissa by detecting the leading one by locally one-dimensional method in this module.
We adjusted the resulting exponent accordingly. Then, we gave the result in IEEE-754 format.
We then checked the result for Underflow and Overflow.
This module had an accuracy of 99.75% on the test bench.

## Slide 13
This is the Block diagram of the complete Addition-Normalizer Module

## Slide 14: Multiplier Module:
Multiplies the mantissas of A and B.
The speed of the operation is determined by the 24*24 bit multiplier which is used to calculate the resulting 48 bit mantissa.
Since, this is the most intensive operation, it is the slowest hence, the rate determining step.

## Slide 15
This is the Block diagram of the complete Multiplier Module

## Slide 16
This is the Block diagram of the complete Multiplication-Normalizer Module

## Slide 17: Divider Module:
We first shift the dividend by 1 towards the left. Then, we subtract the divisor.
We then place the carry as the Least Significant Bit of the intermediate answer. We do this procedure 24 times.

## Slide 18
This is the Block diagram of the complete Divider Module

## Slide 19: Reciprocal Module:
This module was used to calculate the reciprocal of B.
Together with the Multiplier Module, this gives the Divider Module.
Its result had to be checked and handled for Underflow and Overflow.

## Slide 20
This is the Block diagram of the complete Reciprocal Module

## Slide 21: ALU as a whole

## Slide 22
This is the Block diagram of the complete ALU

## Slide 23: Simulation Results
Let’s discuss the Simulation Results of our testbenches.
3

## Slide 24: Accuracy
We ran around 1000 tests each for each operation’s testbenches.
Except Multiply, Divide, we received very high accuracies for all of our operations.
The problem of Overflow and Underflow plagued the Multiply and Divide operations.

## Slide 25
The Accuracy results for all of the testbenches
Operation Name (Code) | Total no. of tests failed | Total no. of tests passed | Total no. of tests failed | Accuracy (in %)
Addition (000) | 1000 | 998 | 2 | 99.8%
Subtraction (001) | 1000 | 997 | 3 | 99.7%
Multiplication (011) | 1000 | 752 | 248 | 75.2%
Division (010) | 1000 | 766 | 234 | 76.6%
Bitwise-AND (100) | 1000 | 1000 | 0 | 100%
Bitwise-OR (101) | 1000 | 1000 | 0 | 100%
Bitwise-NOT (110) | 1000 | 1000 | 0 | 100%

## Slide 26: Waveforms
We ran the simulations on Vivado with a clock of time period 1ns.
We got the Waveforms for all of our test benches.

## Slide 27: Addition Waveform:

## Slide 28: Subtraction Waveform:

## Slide 29: Multiplication Waveform:

## Slide 30: Division Waveform:

## Slide 31: Bitwise AND Waveform:

## Slide 32: Bitwise OR Waveform:

## Slide 33: Bitwise NOT Waveform:

## Slide 34: Summary
The Floating-Point Single-Precision ALU has been discussed extensively in depth.
A suitable algorithm has been developed to successfully carry out various arithmetic and logic operations.
The algorithm has been implemented in a pipelined way so as to minimize delay and maximize computational efficiency.

## Slide 35: Project Team Members
4

## Slide 36: Aaryan Garg
19116001
1

## Slide 37: Sagnik Majumdar
19116063
2

## Slide 38: Pereira Smith
19116047
3

## Slide 39: Divyank Beniwal
19116022
4